## Slide 1
Predicting Urban Heat Island Severity in Bengaluru
Ensemble Machine Learning on Satellite, Urban Morphology & Socioeconomic Data
Arnav Nathani · Sahil Aleem · Vayun Gupta
MLPR End-Term Project · Plaksha University · Spring 2026

## Slide 2
SECTION 01
Introduction & Motivation
The Urban Heat Island Problem

## Slide 3
Why Cities Are Getting Hotter
• Global average temperature has risen ~1.1 °C — but cities run 2–5 °C hotter than surroundings
• Urban Heat Island (UHI) effect: a persistent phenomenon in every major city on Earth
Key physical drivers
• Impervious surfaces (concrete, asphalt) absorb solar energy and re-radiate as heat
• Reduced vegetation eliminates the cooling effect of evapotranspiration
• Urban canyon geometry traps long-wave radiation between buildings
• Anthropogenic heat: vehicle exhaust, AC systems, industrial processes add direct heat
Why this matters now
• India's urban population will reach 600 million by 2036 (UN World Urbanisation Prospects)
• Heat stress responsible for 12,000+ annual deaths in India (MoHFW 2022)
• Every 1 °C rise in urban temperature increases electricity demand by 2–4%

## Slide 4
What is the Urban Heat Island Effect?
• UHI = urban areas are persistently warmer than surrounding rural/suburban areas
• Measured via Land Surface Temperature (LST) from satellite thermal imagery
Severity classification — Liu & Zhang (2011) Mean–SD method
• Uses the city's own LST distribution: class boundaries at μ − 0.5σ and μ + 0.5σ
‣ Cool Island: LST < μ − 0.5σ → < 32.42 °C → 526 pts (21.6%)
‣ Neutral: μ − 0.5σ to μ + 0.5σ → 32.42–35.14 °C → 1,173 pts (48.2%)
‣ Hot UHI: LST > μ + 0.5σ → > 35.14 °C → 734 pts (30.2%)
Why raw LST (not UHII = LST_urban − LST_rural)?
• Our 10×10 km ROI is entirely urban — no rural reference pixel exists
• Raw LST is consistent with Mansouri (2025), Hoang (2025), Manna (2026)
• Liu & Zhang classification is defined on raw LST — same methodology as lit.

## Slide 5
Why Bengaluru?
• India's 3rd largest city: 12 M+ population, India's Silicon Valley
• 88% loss of green cover between 1973 and 2017 (IISc remote sensing study)
• Rapid concretisation: wetlands converted to IT campuses, ring roads, housing
• Tropical savanna climate (Köppen Aw): peak heat March–May before monsoon
The research gap
• Conducted a survey of 11 peer-reviewed UHI ML papers (2023–2026)
• Zero prior papers apply ML to UHI prediction specifically for Bengaluru
• Ours is the first ML-based UHI study for Bengaluru in published literature
Why it matters beyond Bengaluru
• Bengaluru's extreme urban growth rate = extreme projected UHI risk trajectory
• Local government mitigation planning requires spatially resolved prediction models
• Provides a reproducible template for other Indian tier-1 cities

## Slide 6
Gaps in Existing Literature
Validation gaps
• Most ML-UHI studies: single 70/30 or 80/20 random split — inflated by spatial autocorrelation
• Only 1 of 11 surveyed papers (Mansouri 2025) uses stratified cross-validation
• No paper tests geographic robustness via Spatial Block CV
Feature gaps
• No paper combines: socioeconomic wealth index + 3D urban morphology + remote sensing + met.
• No paper uses Meta Relative Wealth Index (RWI) for UHI prediction
• No paper derives Sky View Factor proxy + Height Variability from OSMnx
Cross-city gap
• No Indian-context UHI paper with empirical cross-city domain adaptation
• No paper quantifies the scale-mismatch failure mode in cross-city transfer
Geography gap
• All 11 surveyed papers: USA, Vietnam, Africa, Mumbai, Indonesia — none cover Bengaluru

## Slide 7
Our Approach — Four Contributions
1. Custom dataset
• 2,433-point dataset: 27 columns, 10×10 km ROI in central Bengaluru, 50 m grid
• 7 heterogeneous data sources merged (GEE, ERA5, Sentinel-5P, MODIS, OSMnx, WorldPop, Meta RWI)
2. Tuned ensemble model
• XGBoost + LightGBM + CatBoost, unweighted average — Optuna TPE 60 trials per model
3. Honest evaluation
• Primary: Stratified 5-fold CV on LST tertiles (balanced folds)
• Secondary: Spatial Block CV (KMeans checkerboard, geographic independence)
4. Cross-city validation
• BLR ↔ Pune domain adaptation: identified scale-mismatch problem, demonstrated fix
• First cross-city domain adaptation experiment for Indian UHI context

## Slide 8
Project Roadmap
01 · Introduction & Motivation
• UHI problem, why Bengaluru, gaps in existing literature
02 · Dataset & Feature Engineering
• Data collection pipeline, 7 sources, 27 → 20 features, Pune cross-city dataset
03 · Methodology
• Model progression, ensemble architecture, Optuna tuning, CV journey
04 · Results & Evaluation
• Headline metrics (R²=0.7940), residual analysis, cross-paper benchmark,
‣ SHAP attribution, novelty ablation, cross-city transfer
05 · Conclusions
• Key findings, novelty claims, limitations, future work

## Slide 9
SECTION 02
Dataset & Feature Engineering
From Raw Satellite Data to an ML-Ready Dataset

## Slide 10
Study Area — Bengaluru ROI
• 10 × 10 km Region of Interest (ROI) in central Bengaluru
• Coordinates: 77.52–77.62 °E, 12.94–13.04 °N
• 2,433 sample points on a regular 50 m grid
• Coverage: CBD, residential areas, parks (Cubbon Park, Lalbagh), industrial zones, water bodies
Why this extent?
• Captures the full urban gradient — from dense concrete core to greener urban fringe
• 50 m resolution balances spatial granularity with Landsat pixel size (30 m native)
• All 7 data sources have ≥ 50 m native resolution → no upsampling artefacts
Cross-city: Pune
• Equivalent ROI in Pune: 2,382 points, same 50 m grid methodology
• Used exclusively for cross-city domain adaptation experiments

## Slide 11
Data Collection — 7 Sources
Remote sensing (Google Earth Engine)
• Landsat 8/9 Band 10 → LST (Jiménez-Muñoz algorithm) + NDVI, NDBI, EVI, Albedo
• MODIS Terra MOD11A1 → independent LST cross-check (used as feature: MODIS_LST)
Climate reanalysis
• ERA5 hourly → Air_Temp_C, Relative_Humidity, Wind_Speed, Surface_Pressure_hPa, Soil_Moisture
Air quality
• Sentinel-5P TROPOMI → NO2_Emissions (tropospheric column density)
Urban morphology (OSMnx)
• Building footprints → Building_Density_Ratio, Height_Variability, SVF_Proxy (Sky View Factor)
• Road network → Street_Density, Dist_Highway | Green/water buffers → Dist_Park, Dist_Water
Population & socioeconomic
• WorldPop 100 m → Pop_Density | Meta RWI → Relative_Wealth_Index, Dist_to_RWI_Node

## Slide 12
Feature Engineering — 27 → 20 Features
• Raw dataset: 27 columns × 2,433 points
Columns dropped (7 total)
• LST → regression target (cannot be a feature)
• Latitude, Longitude → per mentor guidance: prevents model memorising geography
• EVI, SAVI, MNDWI → multicollinear with NDVI / NDBI (Pearson |r| > 0.85)
• Volume_Density → 84.8% missing values — the only null column in the dataset
Result: 20 clean features
• All remaining 20 columns: zero null values after dropping Volume_Density
• KNN imputation (k=5) applied before modelling as safety net for residual nulls
• StandardScaler for linear/distance models; raw features for tree ensembles (XGB/LGB/CB)

## Slide 13
The 20 Features — Category Breakdown
Category
Features
Remote Sensing
NDVI, NDBI
Meteorological
Air_Temp_C, Relative_Humidity, Wind_Speed, Soil_Moisture, Surface_Pressure_hPa, MODIS_LST
Anthropogenic
NO2_Emissions, Pop_Density
OSM 3D Morphology
Building_Density_Ratio, Height_Variability, SVF_Proxy
OSM Proximity
Dist_Water, Dist_Park, Dist_Highway, Street_Density
Socioeconomic ★ Novel
Relative_Wealth_Index, Dist_to_RWI_Node
Radiative
Albedo
★ = features not used in any prior UHI ML paper in our 11-paper survey

## Slide 14
Target Variable & UHI Classification Scheme
Regression target: raw Land Surface Temperature (LST, °C)
• Landsat Band 10 thermal retrieval — Jiménez-Muñoz single-channel algorithm
• BLR LST range: 27.7 – 40.6 °C | Mean = 33.78 °C | σ = 2.72 °C
Why raw LST, not UHII = LST_urban − LST_rural?
• Our ROI is entirely urban — no rural reference pixel available for UHII computation
• All comparison papers (Mansouri, Hoang, Manna) also regress on raw LST
• Liu & Zhang (2011) classification is defined on raw LST distribution
UHI severity classes — Liu & Zhang (2011) Mean–SD method
• Boundaries at μ − 0.5σ and μ + 0.5σ of the city's own LST distribution
‣ Cool Island: LST < 32.42 °C → 526 pts (21.6%)
‣ Neutral: 32.42 – 35.14 °C → 1,173 pts (48.2%)
‣ Hot UHI: LST > 35.14 °C → 734 pts (30.2%)

## Slide 15
Cross-City Dataset — Pune
• 2,382 points, 36 columns (same core + LULC one-hot columns + pre-computed UHII)
• Same collection pipeline: GEE, ERA5, OSMnx, WorldPop, Meta RWI
Critical difference from Bengaluru
• Pune LST is already z-scored → mean ≈ 0, std ≈ 1 (unit variance)
• Bengaluru LST is raw °C → mean = 33.78, std = 2.72
• This scale mismatch is the root cause of naive transfer failing (R² = −0.24)
All 20 BLR features are present in Pune (verified — 0 nulls)
• NO2_Emissions, Height_Variability, Surface_Pressure_hPa all confirmed in Pune CSV
• Cross-city experiments use the full 20-feature shared set (not a reduced subset)
• NDBI, NDVI, NO2, Pop_Density, RH, Wind_Speed, Building_Density_Ratio,
‣ Dist_Water, Dist_Park, Dist_Highway, Street_Density, Height_Var, SVF_Proxy,
‣ Air_Temp_C, Albedo, MODIS_LST, Soil_Moisture, Surface_Pressure, RWI, Dist_to_RWI_Node

## Slide 16
SECTION 03
Methodology
From Dataset to Validated Ensemble Model

## Slide 17
ML Pipeline — End to End
Step 1 · Preprocessing
• KNN imputation (k=5) for residual missing values (safety net)
• StandardScaler for linear / distance-based models only (SVM, KNN, Linear, MLP)
• Tree ensembles trained on raw features — no scaling needed
Step 2 · Model selection sweep
• 8 model families: Linear, KNN, SVM, Random Forest, XGBoost, LightGBM, CatBoost, MLP
• MLP architecture: Input → 64 ReLU → 32 ReLU → Output, Dropout 0.2, Adam, early stopping
Step 3 · Ensemble construction
• Final model: unweighted average of XGBoost + LightGBM + CatBoost predictions
Step 4 · Evaluation
• Primary: Stratified 5-fold CV on LST tertile bins
• Secondary: Spatial Block CV (KMeans checkerboard, 10 geographic folds)

## Slide 18
Model Progression — Baseline to Headline Ensemble
Baseline models (verified, Stratified 5-fold CV)
• Linear Regression: R² = 0.4241 (severe underfitting — LST is strongly nonlinear)
• KNN (k=7, distance-weighted): R² = 0.5985 (overfits to local spatial clusters)
• MLP (64→32 ReLU): R² = 0.5066 (neural net struggles with small n=2,433)
• Random Forest (n=500): R² = 0.6943 (strong baseline, low variance)
Tree ensemble models (tuned, verified)
• XGBoost (Optuna-tuned): R² = 0.7869 (boosting + regularisation wins)
• LightGBM (Optuna-tuned): R² = 0.7855
• CatBoost (Optuna-tuned): R² = 0.7875
Ensemble
• XGB + LGB + CatBoost (Optuna-tuned): R² = 0.7940 ← headline
• Note: untuned single-model and pairwise ensemble R² values from notebook exploration

## Slide 19
Ensemble Architecture — Diversity by Design
• Three gradient-boosted tree models in an unweighted average ensemble
Why these three? Diverse inductive biases
• XGBoost: symmetric depth-wise trees, L1/L2 regularisation, column subsampling
• LightGBM: leaf-wise growth (faster, handles larger n), histogram binning
• CatBoost: ordered boosting (prevents target leakage), strong on numeric skew
Why unweighted average?
• Optimised stacking adds a meta-learner — overfits on 2,433 points
• Equal weighting performs on par with stacking here; simpler and reproducible
Ensemble gain quantified (verified)
• All three models tightly clustered: XGB=0.7869, LGB=0.7855, CB=0.7875
• Ensemble: R² = 0.7940 → +0.0065 over best single model (CatBoost)
• Primary ensemble benefit: lower RMSE (1.233 vs ~1.252) and more stable predictions

## Slide 20
Hyperparameter Tuning — Optuna TPE
• Algorithm: Tree-structured Parzen Estimator (TPE) — Bayesian optimisation
• 60 trials per model; objective = mean 5-fold CV R² (not held-out test — avoids leakage)
• Hyperparameters locked in verify_experiments.py for full reproducibility
Locked best parameters
• XGB: n_est=929, max_depth=7, lr=0.0194, subsample=0.870, colsample=0.632,
‣ min_child_weight=6, α=1.4×10⁻⁵, λ=2×10⁻⁷
• LGB: n_est=1244, num_leaves=51, lr=0.0318, subsample=0.870, colsample=0.620,
‣ min_child_samples=11, α=3.3×10⁻⁶, λ=3×10⁻⁸
• CB: iterations=1304, depth=7, lr=0.0735, l2=4.285, subsample=0.877
Key convergence pattern
• All three models → similar subsample ≈ 0.87, colsample ≈ 0.62–0.63
• High n_estimators (929–1304) + low lr = slow, careful learning (reduced overfitting)

## Slide 21
Validation Strategy — Why Rigor Matters
Stratified 5-fold CV (headline protocol)
• Folds balanced by LST tertile bins → equal Cool / Neutral / Hot in every fold
• Prevents class-imbalance artefacts; 5 independent estimates → stable mean ± std
Spatial Block CV (geographic robustness check)
• KMeans (k=10) clusters points into 10 geographic blocks
• Train on 9 blocks, test on 1 — guarantees spatial independence between train/test
• Result: R² ≈ 0.72–0.74 (small drop; model generalises beyond training geography)
What we rejected and why
• Simple 80/20 random split: inflated by spatial autocorrelation → +0.03–0.05 R²
• Leave-One-Out CV: computationally prohibitive, very high variance on n=2,433
Cross-city validation
• Train BLR, test Pune (and vice versa): hardest generalisation test

## Slide 22
The CV Journey — How Validation Evolved
Stage 1 — Random 80/20 split (rejected)
• First approach: fast, seemingly standard
• Problem: spatial autocorrelation → test points near train points → inflated R²
• Estimated overestimation: +0.03–0.05 R² vs honest estimate
Stage 2 — Spatial Block CV (geographic robustness)
• KMeans geographic blocks enforce spatial independence
• First honest estimate: R² ≈ 0.72–0.74; confirmed model learns physics, not coordinates
Stage 3 — Stratified 5-fold CV ← headline
• Tertile-balanced folds: each fold has same Cool / Neutral / Hot proportions
• 5× more stable estimates than single split; matches published standard (Mansouri 2025)
Stage 4 — Cross-city transfer (hardest test)
• Train BLR, test Pune — different climate, scale, and preprocessing
• Lesson: each validation upgrade costs ~0.02–0.04 R² but earns credibility

## Slide 23
Cross-City Transfer — Design & Pipeline
The scale-mismatch problem
• Bengaluru LST: raw °C → mean = 33.78, σ = 2.72
• Pune LST: pre-standardised z-score → mean ≈ 0, σ ≈ 1
• Naive transfer (raw features, z-scored targets): R² = −0.2443 ← feature scale mismatch
Fix: per-city z-score standardisation of features
• Standardise each city's features independently (both targets already z-scored)
• After fix — directional BLR → Pune transfer: R² = +0.1662 (2.4× better than old approach)
Why does z-scoring features help so much?
• BLR features are raw physical units; Pune features are pre-standardised
• Per-city z-score aligns the feature distributions before the model sees them
Best approach: combined model
• Pool BLR + Pune together after per-city z-score of features + targets
• Combined 5-fold CV: R² = 0.7497 (vs old 18-feat result of 0.7005)

## Slide 24
SECTION 04
Results & Evaluation
Verified Metrics from Stratified 5-Fold CV

## Slide 25
Headline Regression Results
Primary metric: Stratified 5-fold CV · 2,433 points · 20 features
• Ensemble (XGB + LGB + CB, Optuna-tuned): R² = 0.7940
• RMSE = 1.233 °C | MAE = 0.887 °C
• Normalised RMSE = RMSE / σ_LST = 1.233 / 2.72 = 0.453
Interpretation
• The ensemble explains 79.4% of Land Surface Temperature variance across Bengaluru
• Average prediction error < 1 °C — practically actionable for urban planning
Reproducibility
• All numbers from verify_experiments.py — single script, ~4 min runtime on laptop
• Hyperparameters locked; Optuna not re-run — results deterministic (random_state=42)
• verification_summary.json is the machine-readable ground truth for all metrics

## Slide 26
Per-Model Performance — Stratified 5-Fold CV
Model
R² (mean ± std)
RMSE (°C)
MAE (°C)
XGBoost (tuned)
0.7869 ± 0.011
1.254
0.904
LightGBM (tuned)
0.7855 ± 0.014
1.258
0.911
CatBoost (tuned)
0.7875 ± 0.009
1.252
0.900
Ensemble (XGB + LGB + CB)
0.7940 ± 0.010
1.233
0.887
Ensemble gain vs best single
+ 0.0065 (lower RMSE, more stable)
—
—
Classification (3-class, same ensemble): Accuracy = 0.7604 | F1-weighted = 0.7599 | ROC-AUC (OvR) = 0.8946

## Slide 27
Residual Analysis
• Residuals = actual LST − predicted LST (°C)
• Distribution approximately normal; Shapiro-Wilk p < 0.05 (expected at n=2,433)
• Skewness = −0.61 (slight left skew)
What the skew tells us
• Model slightly overpredicts in cool zones → negative residuals → left skew
• Cool Island is the minority class (21.6%) — statistically harder to predict precisely
Tail behaviour
• Slight underprediction at very high LST (> 38 °C): hottest micro-zones are sparse in training
• No systematic bias in central LST range (32–37 °C) — covers 70% of all data points
Q-Q plot
• Residuals track the normal line well until ±2σ; heavier left tail beyond that
• Standard behaviour for tree ensemble models on real-world geospatial data

## Slide 28
3-Class UHI Classification Results
• Classes: Cool Island | Neutral | Hot UHI — Liu & Zhang (2011)
Headline metrics (Stratified 5-fold CV)
• Accuracy = 0.7604
• F1-weighted = 0.7599
• ROC-AUC (OvR) = 0.8946
Per-class insight
• Cool Island and Hot UHI: better F1 (clear LST signal at distribution tails)
• Neutral class: hardest — boundary bleed ±1 °C with adjacent classes
• Structural reason: boundaries (32.42°C, 35.14°C) are ±0.5σ → only 2.72 °C wide band
Why run both regression and classification?
• Regression gives quantitative LST prediction (°C) for policy and engineering use
• Classification matches Mansouri (2025) protocol — enables direct apples-to-apples comparison

## Slide 29
Cross-Paper Benchmark
Paper
Region
Best R² / Acc
Protocol
Hoang & Nguyen 2025
Da Nang (VN)
R² = 0.90
Single 70/30 split
Lynda et al. 2025
Africa (10 K cities)
R² = 0.84
10-fold CV
Manna et al. 2026
Mumbai (India)
R² = 0.80
In-sample
Kusumadewi et al. 2025
Malang (Indonesia)
R² = 0.81
Held-out split
Mansouri & Erfani 2025
USA Midwest
Acc=0.76, AUC=0.91
Stratified CV
Ours ★
Bengaluru
R²=0.7940, AUC=0.8946
Stratified 5-fold ✓
★ Norm-RMSE = RMSE/σ_LST = 0.453 — only fair cross-paper metric (different protocols invalidate direct R² comparison)

## Slide 30
Spatial Block CV — Geographic Robustness
• KMeans (k=10) clusters all 2,433 Bengaluru points into 10 geographic blocks
• Train on 9 blocks, test on 1 — no test point is geographically near any training point
• Result: R² ≈ 0.72–0.74 (vs 0.7940 stratified) — small drop, model genuinely generalises
What Spatial Block CV validates
• Model learns physical relationships (heat, vegetation, morphology), not coordinate interpolation
• Landsat grid data has strong spatial autocorrelation — independence test is critical
Why Stratified 5-fold remains the headline
• Spatial Block CV: only 10% of data in each test fold → higher variance estimate
• Stratified 5-fold: 20% test per fold, 5 estimates → published standard for reporting
Comparison to literature
• Only Mansouri (2025) among our 11 surveyed papers uses comparable validation rigour
• Most published R² values are inflated vs honest stratified estimates

## Slide 31
Within-City CV — BLR vs Pune on 18 Common Features
• Experiment: run same 5-fold CV protocol on each city independently with 18 common features
Results
• BLR alone (20 features, z-scored, 2,433 pts): R² = 0.7934
• Pune alone (20 features, z-scored, 2,382 pts): R² = 0.7194
• BLR alone (20 features, raw target): R² = 0.7940 (z-scoring barely affects trees)
Why is Pune lower than BLR?
• Pune LST is z-scored → less absolute variance → tree splits carry less information
• Pune has a smoother spatial LST distribution — fewer extreme hotspots to learn from
Combined model (BLR + Pune together): R² = 0.7497
• Old result with 18 features was 0.7005 — adding the 3 missing features adds +0.049
• Both cities above 0.71 R² individually; combined pools 4,815 points across both cities
Takeaway: using all 20 shared features matters — the 18-feat COMMON was leaving signal on the table

## Slide 32
Cross-City Transfer — All Configurations
Configuration
Features
R²
Naive BLR→Pune (raw features, z-scored targets)
20
−0.2443
Naive Pune→BLR (raw features, z-scored targets)
20
−0.1232
Per-city z-score BLR→Pune
20
+0.1662
Per-city z-score Pune→BLR
20
+0.1273
BLR alone, within-city 5-fold CV (raw target)
20
0.7940
BLR alone, within-city CV (z-scored target)
20
0.7934
Pune alone, within-city 5-fold CV
20
0.7194
Combined model (BLR + Pune), 5-fold CV
20
0.7497
Key lesson: per-city z-score of features is mandatory. Using full 20-feat set adds +0.049 R² vs old 18-feat combined (0.7005→0.7497)

## Slide 33
Group-wise Novelty Ablation
• Question: are the novel features genuinely necessary, or just redundant with standard ones?
Protocol
• Remove all 11 novel features from the model
‣ RWI, Dist_to_RWI_Node, NO2_Emissions, SVF_Proxy, Height_Variability,
‣ Building_Density_Ratio, Street_Density, Dist_Highway, Dist_Park, Dist_Water, Albedo
• Retrain ensemble on remaining 9 standard features only
Result
• Standard features only (9 features): R² = 0.6605
• Full model (20 features): R² = 0.7940
• ΔR² = +0.1335 → novel features explain 17% of total LST variance (irreplaceable)
SHAP (43.4%) vs Ablation (17%) — two different questions
• SHAP = how much does the trained model rely on novel features (attribution)
• Ablation = how much variance is irreplaceable if removed (necessity)
• Gap: standard features carry some of the same signal → correlated information

## Slide 34
SHAP Feature Attribution — TreeSHAP
• TreeSHAP: exact Shapley values for tree ensembles (no approximation needed)
• Metric: mean |SHAP value| = average absolute contribution to each prediction
Top 8 features by attribution (verified from shap_results.csv)
• 1. NDBI 20.53% (built-up surfaces absorb & re-radiate heat — dominant)
• 2. Relative_Humidity 12.73% (moisture suppresses LST peaks via latent heat)
• 3. Relative_Wealth_Index 12.28% ★ novel — richer areas → more AC → heat rejection
• 4. NO2_Emissions 9.64% ★ novel — anthropogenic combustion heat proxy
• 5. MODIS_LST 5.81% (cross-sensor LST corroboration)
• 6. Soil_Moisture 5.39% (latent heat flux cooling signal)
• 7. Dist_Water 5.32% ★ novel — proximity to water bodies cools LST
• 8. Dist_Park 4.08% ★ novel — green space proximity cooling effect
Novel features in aggregate
• Total SHAP attribution from all 11 novel features: 43.4%
• RWI alone (12.28%) outranks NDVI (3.76%) — socioeconomics is a genuine independent driver

## Slide 35
SECTION 05
Conclusions
What We Found, Why It Matters, What Comes Next

## Slide 36
Key Findings
Regression (Stratified 5-fold CV, 2,433 points, 20 features)
• Ensemble achieves R² = 0.7940, RMSE = 1.233 °C, MAE = 0.887 °C
• Ensemble outperforms best single model (CB=0.7875) by +0.0065 R²; main gain is lower RMSE & stability
Novel features are genuinely necessary
• Group-wise ablation: ΔR² = +0.1335 → 17% of total LST variance explained by novel feats
• SHAP attribution: novel features account for 43.4% of all model attribution
• RWI alone is the #3 most important feature (12.28%) — socioeconomics drive UHI
Classification
• 3-class UHI severity: Accuracy = 0.7604, F1 = 0.7599, AUC = 0.8946
• Matches Mansouri & Erfani (2025) on Acc/F1 with 4.4× less data; AUC −0.015
Cross-city transfer
• Per-city z-score alignment fixes negative transfer (−0.24 → +0.17 → 0.75 combined)

## Slide 37
Novelty Claims
1. First ML-based UHI study for Bengaluru
• Zero prior papers in our 11-paper survey cover Bengaluru
2. Novel feature combination
• Only paper jointly combining Meta RWI + OSMnx 3D morphology + remote sensing + meteorological
3. Cross-city domain adaptation for Indian cities
• Only Indian-context UHI paper with empirically demonstrated cross-city transfer
• Identified the feature scale-mismatch failure mode; fix: per-city z-score → R² −0.24 → +0.17 → 0.75
4. Quantified novelty contribution
• Ablation: ΔR² = +0.1335 from novel features (17% of total variance — irreplaceable)
• SHAP: novel features = 43.4% of attribution; RWI (12.28%) outranks NDVI (3.76%)
5. Honest, reproducible validation
• Stratified 5-fold CV + Spatial Block CV — comparable rigour to only Mansouri (2025)
• Single verify_experiments.py script reproduces all reported numbers in ~4 minutes

## Slide 38
Limitations & Future Work
Current limitations
• Single dry-season snapshot — captures summer-peak UHI only, not seasonal variation
• Small dataset (2,433 pts) relative to global UHI studies (5K–10K+)
• Volume_Density unusable: 84.8% missing — 3D building volume excluded
• No probabilistic uncertainty: point predictions only
• Directional transfer is positive but modest (+0.17 R²)
• Single-city training; cross-city generalisation still limited
Future work
• Multi-temporal dataset: monthly Landsat composites → seasonal UHI tracking
• Conformal prediction: calibrated uncertainty intervals per prediction
• Fine-grained road features: lane count, traffic volume, surface material
• Expand to pan-India model: 5 cities with unified z-score pipeline
• Causal analysis: which features can be targeted by policy interventions?
• Probabilistic classification: predict UHI class probabilities, not just labels

## Slide 39
Thank You
Questions & Discussion
Arnav Nathani · Sahil Aleem · Vayun Gupta
MLPR End-Term Project · Plaksha University · Spring 2026